## Slide 1: Internet of bins
Georgi Dimitrov, Adriano Izzi, Lorenzo Frangella

## Slide 2: Project development core parts
networking
The communication algorithm developed.
Sensors deployment
Sensors used in the project development
ALarms and regression
The nodes send alarms and adjust parameters

## Slide 3: Overview - Networking protocol
Nodes self organize themselves in a structured DAG topology to exchange messages. The Root bin has also acts as gateway.

## Slide 4: Algorithm - Networking protocoL
First of all, they wake up at the start of the round trough RTC
WAKE UP!
LV 0
LV 1
LV 2
LV 3

## Slide 5: Algorithm - Networking protocoL
For five seconds, all nodes make measurements
MEASURE
LV 0
LV 1
LV 2
LV 3
MEASURE
MEASURE
MEASURE

## Slide 6: Algorithm - Networking protocoL
Based on level and time windows, they send and receive messages in the Forward round
SEND
RECEIVE
LV 0
LV 1
LV 2
LV 3
MEASURE
MEASURE
MEASURE
MEASURE

## Slide 7: Algorithm - Networking protocoL
Based on level and time windows, they send and receive messages in the Forward round
SEND
RECEIVE
LV 0
LV 1
LV 2
LV 3
MEASURE
MEASURE
MEASURE
MEASURE
SEND
RECEIVE

## Slide 8: Algorithm - Networking protocoL
Based on level and time windows, they send and receive messages in the Forward round
SEND
RECEIVE
LV 0
LV 1
LV 2
LV 3
MEASURE
MEASURE
MEASURE
MEASURE
SEND
RECEIVE
SEND
RECEIVE

## Slide 9: Algorithm - Networking protocoL
The level 0 node, the gateway, trasmit the alarms trough MQTT
LV 0
LV 1
LV 2
LV 3
TRANSMIT
SEND
RECEIVE
MEASURE
MEASURE
MEASURE
MEASURE
SEND
RECEIVE
SEND
RECEIVE

## Slide 10: Algorithm - Networking protocoL
During Response round, starting from the gateway, the nodes quickly receive and send messages to synchronyze RTC
LV 0
LV 1
LV 2
LV 3
SYNC
SYNC
SYNC
SYNC
TRANSMIT
SEND
RECEIVE
MEASURE
MEASURE
MEASURE
MEASURE
SEND
RECEIVE
SEND
RECEIVE

## Slide 11: Algorithm - Networking protocoL
The nodes sleep, waiting for the next round…
WAKE UP!
LV 0
LV 1
LV 2
LV 3
LIGHT SLEEP…
SYNC
SYNC
SYNC
SYNC
TRANSMIT
SEND
RECEIVE
MEASURE
MEASURE
MEASURE
MEASURE
SEND
RECEIVE
SEND
RECEIVE
LIGHT SLEEP…
LIGHT SLEEP…
LIGHT SLEEP…

## Slide 12: key concepts - Networking protocol
A new node start overhearing waiting for sync messages
A node level is defined by the lowest node it can hear trough LoRa
The maximum level of the tree is 4, since it can cover over 40 km of diameters
Nodes send their message only if there is an alarm
Nodes send all message they have received in that Forward round

## Slide 13: Security - Networking protocol
All nodes share a secret key to create and verify hashes
Not harcoded into the .elf
Trasmitted trough bluetooth when the bin is installed (special app has been developed for that)
Used toghether with message details to create hash
Used toghether with message details to verify hashes
During installation, the key is…
At runtime, the key is…

## Slide 14: development - Networking protocol
Originally, the protocol was much more complex and dynamic.
It was able to sustain an arbitrary number of levels and dynamic topologies.
Yet, due to minor but unfixable bugs related to LoRa (they eluded us for two weeks), we decided to simplify it and focus on other parts of the project.
The old code is avaiable to read trough Github commits

## Slide 15: Types - SENSORS
TEMPERATURE
To avoid the insurgence of fire
Filling level
Ultrasound sensors to measure distance from the top of the bin to the garbage
Time
To know time passed since last collection and avoid foul smells
Bad Gas level
Gas sensors to
detect foul smells

## Slide 16: Employed - SENSORs
TEMPERATURE
To avoid the insurgence of fire
Filling level
Ultrasound sensors to measure distance from the top of the bin to the garbage
Time
To know time passed since last collection and avoid foul smells
Bad Gas level
Gas sensors to
detect foul smells

## Slide 17: Employed - SENSORs
TEMPERATURE
To avoid the insurgence of fire
Filling level
Ultrasound sensors to measure distance from the top of the bin to the garbage
Time
To know time passed since last collection and avoid foul smells
Bad Gas level
Gas sensors to
detect foul smells

## Slide 18: Employed - SENSORs
TEMPERATURE
To avoid the insurgence of fire
Filling level
Ultrasound sensors to measure distance from the top of the bin to the garbage
Time
To know time passed since last collection and avoid foul smells
Bad Gas level
Gas sensors to
detect foul smells

## Slide 19: Employed - SENSORs
TEMPERATURE
To avoid the insurgence of fire
Filling level
Ultrasound sensors to measure distance from the top of the bin to the garbage
Time
To know time passed since last collection and avoid foul smells
Bad Gas level
Gas sensors to
detect foul smells

## Slide 20: Employed - SENSORs
TEMPERATURE
To avoid the insurgence of fire
Filling level
Ultrasound sensors to measure distance from the top of the bin to the garbage
Time
To know time passed since last collection and avoid foul smells
Bad Gas level
Gas sensors to
detect foul smells

## Slide 21: Employed - SENSORs
TEMPERATURE
To avoid the insurgence of fire
Filling level
Ultrasound sensors to measure distance from the top of the bin to the garbage
Time
To know time passed since last collection and avoid foul smells
Bad Gas level
Gas sensors to
detect foul smells

## Slide 22: alarms - SENSORS
TEMPERATURE
Under 40°, nothing
40° - 50°, alert
Over 50°, alarm
Filling level
Uses dynamic calculation to send alert
If above 85%, send alarm
Time
Interrupt on pin 25 when time to wake up
Bad Gas level
Uses temperature and time passed to send alert
If above treshold, send alarm

## Slide 23: Filling level thresholds - SENSORS
The filling level tresholds dynamically reconfigure over time.
Filling rate since last gathering
Average time passed between gathering
If
then send alert
If Filling level is above 85%, send alarm
Node keeps track of:
Tresholds are:

## Slide 24: Server side - Mqtt
We used a MQTT protocol (actually HiveMQ) to send messages from the gateway and read them server side.
Geodata of the bins (taken at configuration time) and alarms can be used by other services to implement trash gathering

## Slide 25: Standard node - Consumption
Here we can see the following phases:
Activation
Bluetooth
Discovering
Light Sleep
Measuring
Receiving
Sending
Sync
Light Sleep

## Slide 26: Standard node No Sensors - Consumption
Here we can see the following phases:
Receiving
Sync
Light Sleep

## Slide 27: Gateway activation no sensors - Consumption
Here we can see the following phases:
Bluetooth
Wifi
SNTP

## Slide 28: Energy and POwer- Consumption
Assuming that the system wake up each hour, the average energy consumption for hour is:
=
=
380.200 mW
So the average power consuption for a day is 105,5 mW.
So if we want to power the system for few days we need a battery of:

## Slide 29: Energy and POwer- Consumption
Since we need the bins to be active for years, we assume that there is a mechanism for energy harvesting to recharge the batteries.

## Slide 30: Thanks for the attention!